## Slide 1: Datum Transformations in Qgis @GeoDev #5
Anja Vrecko
anja.vrecko@sinergise.com

## Slide 2: Scope
Datum transformations
  Some theory
  How I approached it in Qgis
Out of scope
  Coordinate systems in general
  How to chose a right projection for my purpose
  V datums

## Slide 3: Problem

## Slide 4: Problem

## Slide 5: Problem
Approx. 8 m mismatch between RABA and Open Street Map (map is shown in EPSG:3785) – can 8 m discrepancy be a consequence of less accurate set of transformation parameters?
RABA has no coordinate reference system (CRS) specified but it was assumed it is in „old“ Slovenian reference coordinate system
Some kind of transformation was happening but it was not clear what parameters are being used

## Slide 6: What I knew:
GURS provides transformation parameters per region or for the whole country. Accuracy for the whole country is cca 1,25 m.
http://www.e-prostor.gov.si/zbirke-prostorskih-podatkov/drzavni-koordinatni-sistem/horizontalni-drzavni-koordinatni-sistem-d96tm/#tab6-1026
Common problems with transformations:
  Axis order
  „coordinate frame“ rotation vs „position vector“ rotation
Differences between:
  Earth vs ellipsoid vs projection surface
  Projection vs datum transformation
  Ellipsoid vs datum

## Slide 7: Datum Transformations - Big Picture

## Slide 8: Transformation models
7- parameters Helmert‘s similarity transformation
Bursa-Wolf = Helmert‘s but with simplified rotation matrix:
Molodensky-Badekas= Bursa-Wolf but rotation is around centroid
abridging Molodenski = simplified version, where we model 3 translations only
Sources: https://www.researchgate.net/publication/228757515_A_NOTE_ON_THE_BURSA-WOLF_AND_MOLODENSKY-BADEKAS_TRANSFORMATIONS, http://elte.prompt.hu/sites/default/files/tananyagok/MapGridsAndDatums/ch04s02.html

## Slide 9: But transformation between 2 ellipsoids seems deterministic ...
Datum
Where do the transformation parameters come from?

## Slide 10
How all the theory is implemented (in Qgis)
CRSs have „default“ transformations (TOWGS84)
How to control transformations in Qgis
What I didn‘t know:

## Slide 11: Tools
PROJ
  C:\Program Files\QGIS 3.0\share\proj;
  EPSG
    # Slovenia 1996<4882> +proj=geocent +ellps=GRS80 +units=m +no_defs <>
    # Slovenia 1996<4765> +proj=longlat +ellps=GRS80 +towgs84=0,0,0,0,0,0,0 +no_defs <>
    # MGI / Slovenia Grid (deprecated)<2170> +proj=tmerc +lat_0=0 +lon_0=15 +k=0.9999 +x_0=500000 +y_0=0 +datum=hermannskogel +units=m +no_defs <>
    # MGI / Slovene National Grid (deprecated)<3787> +proj=tmerc +lat_0=0 +lon_0=15 +k=0.9999 +x_0=500000 +y_0=-5000000 +datum=hermannskogel +units=m +no_defs <>
    # Slovenia 1996 / Slovene National Grid<3794> +proj=tmerc +lat_0=0 +lon_0=15 +k=0.9999 +x_0=500000 +y_0=-5000000 +ellps=GRS80 +towgs84=0,0,0,0,0,0,0 +units=m +no_defs <>
    # MGI 1901 / Slovenia Grid<3911> +proj=tmerc +lat_0=0 +lon_0=15 +k=0.9999 +x_0=500000 +y_0=0 +ellps=bessel +towgs84=682,-203,480,0,0,0,0 +units=m +no_defs <>
    # MGI 1901 / Slovene National Grid<3912> +proj=tmerc +lat_0=0 +lon_0=15 +k=0.9999 +x_0=500000 +y_0=-5000000 +ellps=bessel +towgs84=682,-203,480,0,0,0,0 +units=m +no_defs <>
  ESRI
    # MGI / Slovenia Grid<2170> +proj=tmerc +lat_0=0 +lon_0=15 +k=0.999900 +x_0=500000 +y_0=0 +ellps=bessel +units=m +no_defs no_defs <>
GDAL
  3912,"MGI 1901 / Slovene National Grid",9001,3906,19845,9807,1,0,4498,8801,0,9102,8802,15,9102,8805,0.9999,9201,8806,500000,9001,8807,-5000000,9001,,,,,,,,,,,,,
  Gdal datum:
    6765,Slovenia Geodetic Datum 1996,geodetic,"Densification of ETRS89, based on ITRS89 at epoch 1995.55.",1996-01-01,7019,8901,1212,"Geodetic survey, topographic mapping.",,Surveying and Mapping Authority of Slovenia,OGP,"2008/04/04",,0,"D_Slovenia_Geodetic_Datum_1996"
.prj (= WKT representation of CRS, WKT2 is coming but not yet supported in Qgis)

## Slide 12: WKT representation:

## Slide 13: Back to the example:
Old“ Slovenian coordiante reference system: D48/GK ... EPSG 3912
  Transformations:
    EPSG:3962: TOWGS84 [682.0, -203.0, 480.0, 0.0, 0.0, 0.0, 0.0]
    EPSG:3915: TOWGS84 [426.9, 142.6, 460.1, 4.91, 4.49, -12.42, 17.1]
    EPSG:3917: TOWGS84 [ 409.545, 72.164, 486.872, -3.085957, -5.46911, 11.020289, 17.919665] = offical GURS‘s parameters for the whole country
„New“ Slovenian coordiante reference system: D96/TM ... EPSG 3794
Recomended user defined CRS with:
    TOWGS84[476.08,125.95,417.81,4.610862,2.388137,-11.942335,9.896638]
Check out: https://epsg.io/
Source: Sandi Berk, Danijel Boldin: Slovenian coordinate reference systems in GIS environment, http://www.geodetski-vestnik.com/61/1/gv61-1_berk.pdf

## Slide 14: In Qgis show:
1) How to assign CRS to the layer
2) How to get a list of avalaible transformation parameters sets
3.1) Set custom CRS
3.2) Change .prj file
4) Reproject data and save it

## Slide 15: *In Python:
Coordiante transformations in Python:
  pyproj (uses proj.4)
  osgeo (uses gdal)
  How to define your own parameters:
    https://publicwiki.deltares.nl/display/OET/Python+convert+coordinates

## Slide 16: Recommendations:
Control datum transformation
Do not hide important settings
In Qgis the safest option is to define your own CRS (as opposed to tweaking towgs84 parameter)
If possible compare results with:
  Results of higher accuracy transformation (for Slovenia you can use 3tra http://www.e-prostor.gov.si/zbirke-prostorskih-podatkov/drzavni-koordinatni-sistem/transformacija-v-novi-koordinatni-sistem/#tab2-1177)
  OSM proved quite reliable (but check if accuracy is good enough for you)
Use the same parameters for all data sets (you can not do this if you do not know how data was transformed)

## Slide 17
Thank you!